## Slide 1: ECE 424 – Introduction to VLSI Design
Emre Yengel
Department of Electrical and Communication Engineering
Fall 2012

## Slide 2: Standard Cell Layout Methodology
Layout
The Design Rules describe:
Minimum width to avoid breaks in a line
Minimum spacing to avoid shorts between lines
Minimum overlap to ensure two layers completely overlap
Unit Transistor
Transistor dimensions are specified by their W/L ratio
For 0.6 μm process, W = 1.2μm and L = 0.6μm
Such a minimum width contacted transistor is called UNITTRANSISTOR

## Slide 3: Standard Cell Layout Methodology
Inverter Layout
Transistor dimensions specified as Width / Length
•Minimum size is 4 λ /2λ, sometimes called 1 unit
•For 0.6 mm process, W=1.2μm, L=0.6μm

## Slide 4: Standard Cell Layout Methodology
Inverter Cross section with well and substrate contacts

## Slide 5: Standard Cell Layout Methodology

## Slide 6: Standard Cell Layout Methodology

## Slide 7: Standard Cell Layout Methodology

## Slide 8: Standard Cell Layout Methodology
Layout
A conservative but easy to use Design Rules for n-well process is as follows:
Metal and diffusion have minimum width spacing of 4 λ
Contacts are 2 λ X 2 λ and must be surrounded by 1 λ on the layers above and below
Polysilicon uses a width of 2 λ
Polysilicon overlaps diffusion by 2λ where a transistor is desired and has a spacing of 1 λ away where no transistor is desired
Polysilicon and contacts have a spacing of 3λ from other polysilicon or contacts
N-well surrounds PMOS transistors by 6λ and avoids NMOS transistors by 6λ

## Slide 9: Standard Cell Layout Methodology
Rules to get you started;
Simplifed λ based design rules

## Slide 10: Standard Cell Layout Methodology
3 Input NAND Standard cell gate layout

## Slide 11: Standard Cell Layout Methodology
Well Spacing:
Wells must surround transistors by 6 λ
•Implies 12 λ between opposite transistor flavors
•Leaves room for one wire track

## Slide 12: Standard Cell Layout Methodology
A simple method for finding the optimum gate ordering is the Euler-path method: Simply find a Euler path in the pull-down network graph and a Euler path in the pull-up network graph with the identical ordering of input labels, i.e., find a common Euler path for both graphs.
The Euler path is defined as an uninterrupted path that traverses each edge (branch) of the graph exactly once.

## Slide 13: Finding an Euler’s Path
Computer Algorithms:
It is relatively easy for a computer to consider all possible arrangements of transistors in search of a suitable Euler path.
This is not so easy for the human designer.
One Human Algorithm
Find a path which passes through all n-transistors exactly once.
Express the path in terms of the gate connections.
Is it possible to follow a similarly labelled path through the p-transistors?
Yes – you’ve succeeded.
No – try again (you may like to try a p path first this time)

## Slide 14: Finding an Euler’s Path
Vp
a
c
b
b
a
c
Out
x
y
x
y
Vertex
Edge
Vertex
Gnd

## Slide 15: Euler Path

## Slide 16: Stick Diagrams
Stick Diagrams (SD)
VLSI design aims to translate circuit concepts onto silicon.
stick diagrams are a means of capturing topography and layer information using simple diagrams.
Stick diagrams convey layer information through colour codes (or monochrome encoding).
Acts as an interface between symbolic circuit and the actual layout.

## Slide 17: Stick Diagrams
Stick Diagrams;
Does show all components/vias.
It shows relative placement of components.
Goes one step closer to the layout
Helps plan the layout and routing
Stick Diagrams Does not show
•Exact placement of components
•Transistor sizes
•Wire lengths, wire widths, tub boundaries.
•Any other low level details such as parasitics.

## Slide 18: Stick Diagrams
Metal
poly
ndiff
pdiff
Can also draw
in shades of
gray/line style.

## Slide 19: Stick Diagrams

## Slide 20: Example

## Slide 21: Example

## Slide 22: Example

## Slide 23: Example

## Slide 24: Example

## Slide 25: Example

## Slide 26: Example

## Slide 27: Example

## Slide 28: Example

## Slide 29: Example

## Slide 30: Example

## Slide 31: Example

## Slide 32: Example

## Slide 33: Example 2

## Slide 34: Example 3

## Slide 35: Example 3