## Slide 1: ECE 424 – Introduction to VLSI Design
Emre Yengel
Department of Electrical and Communication Engineering
Fall 2014

## Slide 2: Introduction
Sequential circuit
  Output depends not just on present inputs (as in combinational circuit), but on past sequence of inputs
    Stores bits, also known as having “state”
  Simple example: a circuit that counts up in binary
A sequential circuit consists of a feedback path, and employs some memory elements.

## Slide 3: Introduction
a
Flight attendant call button
  Press call: light turns on
    Stays on after button released
  Press cancel: light turns off
  Logic gate circuit to implement this?
Q
Call
Cancel
Doesn’t work. Q=1 when Call=1, but doesn’t stay 1 when Call returns to 0
Need some form of “feedback” in the circuit
a
a
Bit
Storage
Blue light
Call
button
Cancel
button
1. Call button pressed – light turns on
Bit
Storage
Blue light
Call
button
Cancel
button
2. Call button released – light stays on
Bit
Storage
Blue light
Call
button
Cancel
button
3. Cancel button pressed – light turns off

## Slide 4: Memory Elements
There are two types of sequential circuits:
  synchronous: outputs change only at specific time
  asynchronous: outputs change at any time
Multivibrator: a class of sequential circuits. They can be:
  bistable (2 stable states)
  monostable or one-shot (1 stable state)
  astable (no stable state)
Bistable logic devices: latches and registers
  a latch is level sensitive
  a register is edge-triggered
Many books call edge-triggered elements flip-flops.

## Slide 5: Standard Memory Elements
Memory element with clock.
Clock is usually a square wave.
command
Memory element
stored value
Q
clock
Positive edges
Negative edges
Positive pulses

## Slide 6: Timing Definitions
t
t
D
t
c
2
q
t
hold
t
su
t
Q
DATA
STABLE
DATA
STABLE
Register
CLK
D
Q
setup time (tsu) hold time (thold)
propagation delay (tc-q)

## Slide 7: Latches vs Registers
Latch
stores data when clock is low or high
D
Clk
Q
D
Clk
Q
Register
stores data when clock rises
Clk
Clk
D
D
Q
Q

## Slide 8: Latches

## Slide 9: Static Latches and Registers: Bistability Principle
V
i
1
A
C
B
V
o
2
V
i
1
=
V
o
2
V
o1
Vi2
V
i
2
=
V
o
1
When the gain of the inverter in the transient region is larger than 1, only A
and B are stable operation points, and C is a metastable operation point.

## Slide 10
Gain should be larger than 1 in the transition region
Bistability Principle

## Slide 11: SR Latches
0
0
1
R=1
S=0
t
Q
1
0
1
0
R
S
1
0
t
1
0
Q
Q
S (set)
SR latch
R (reset)
Does the circuit to the right, with cross-coupled NOR gates, do what we want?
1
0
0
1
0
1
t
Q
S=0
R=0
t
Q
S=1
R=0
0
1
1
t
Q
R=0
S=0
1
0
1
0
0
0
1
1
X
0
Recall…
a

## Slide 12: SR Latches
Characteristics table for active-high input S-R latch (also known as NOR gate latch):
Characteristics table for active-low input S'-R' latch (also known as NAND gate latch):
S
R
Q
Q'
S
R
Q
Q'

## Slide 13: SR Latches
Problem
  If S=1 and R=1 simultaneously, we don’t know what value Q will take
Q may oscillate. Then, because one path will be slightly longer than the other, Q will eventually settle to 1 or 0 – but we don’t know which.

## Slide 14: SR Latches
Problem not just one of a user pressing two buttons at same time
Can also occur even if SR inputs come from a circuit that supposedly never sets S=1 and R=1 at same time
  But does, due to different delays of different paths
The longer path from X to R than to S causes SR=11 for short time – could be long enough to cause oscillation
R
Y
X
S
SR latch
Q
A
r
bit
r
a
r
y
circuit

## Slide 15: Level Sensitive SR Latches
Add enable input “C” as shown
  Only let S and R change when C=0
    Enure circuit in front of SR never sets SR=11, except briefly due to path delays
  Change C to 1 only after sufficient time for S and R to be stable
  When C becomes 1, the stable S and R value passes through the two AND gates to the SR latch’s S1 R1 inputs.
R1
S1
S
C
R
Level-sensitive SR latch
Q
Though SR=11 briefly...
...S1R1 never = 11
S
C
Q
’
Q
R
Level-sensitive SR latch symbol
R1
S1
S
X
Y
C
Clk
R
Level-sensitive SR latch
Q
0
1
0
1
0
1
0
1
0
S
R
C
S1
R1
1
a

## Slide 16: Clock Signals of a Latch
How do we know when it’s safe to set C=1?
  Most common solution –make C pulse up/down
    C=0: Safe to change X, Y
    C=1: Must not change X, Y
    We’ll see how to ensure that later
  Clock signal -- Pulsing signal used to enable latches
    Because it ticks like a clock
  Sequential circuit whose storage components all use clock signals: synchronous circuit
    Most common type
    Asynchronous circuits – important topic, but left for advanced course
R1
S1
S
X
Y
C
Clk
R
Q
Level-sensitive SR latch

## Slide 17: Clocks
Clock period: time interval between pulses
  Above signal: period = 20 ns
Clock cycle: one such time interval
  Above signal shows 3.5 clock cycles
Clock frequency: 1/period
  Above signal: frequency = 1 / 20 ns = 50 MHz
    1 Hz = 1/s
100 GHz
10 GHz
1 GHz
100 MHz
10 MHz
0.01 ns
0.1 ns
1 ns
10 ns
100 ns
Period
Freq

## Slide 18: Level Sensitive D Latch
SR latch requires careful design to ensure SR=11 never occurs
D latch relieves designer of that burden
  Inserted inverter ensures R always opposite of S
R
S
D
C
D latch
Q
D
Q
’
Q
C
D latch symbol

## Slide 19: Problem with Level-Sensitive D Latch
D latch still has problem (as does SR latch)
  When C=1, through how many latches will a signal travel?
  Depends on for how long C=1
    Clk_A -- signal may travel through multiple latches
    Clk_B -- signal may travel through fewer latches
  Hard to pick C that is just the right length
    Can we design bit storage that only stores a value on the rising edge of a clock signal?
Clk

## Slide 20: Flip-Flop
Flip-flop: Bit storage that stores on clock edge, not level
One design -- master-servant
  Two latches, output of first goes to input of second, master latch has inverted clock signal
  So master loaded when C=0, then servant when C=1
  When C changes from 0 to 1, master disabled, servant loaded with value that was at D just before C changed -- i.e., value at D during rising edge of C
Clk
rising edges
Note: Hundreds of different flip-flop designs exist
D latch
master
D latch
servant
D
Dm
Ds
Cs
Qm
Q
s
’
Qs
Q
Q
’
C
m
Clk
D flip-flop

## Slide 21: Edge-Triggered Flip-Flops
S-R, D and J-K edge-triggered flip-flops. Note the “>” symbol at the clock input.
S
C
R
Q
Q'
S
C
R
Q
Q'
D
C
Q
Q'
D
C
Q
Q'
J
C
K
Q
Q'
J
C
K
Q
Q'
Positive edge-triggered flip-flops
Negative edge-triggered flip-flops

## Slide 22: S-R Flip-Flop
S-R flip-flop: on the triggering edge of the clock pulse,
  S=HIGH (and R=LOW) a SET state
  R=HIGH (and S=LOW) a RESET state
  both inputs LOW a no change
  both inputs HIGH a invalid
Characteristic table of positive edge-triggered S-R flip-flop:
X = irrelevant (“don’t care”)
 = clock transition LOW to HIGH

## Slide 23: S-R Flip-Flop
It comprises 3 parts:
  a basic NAND latch
  a pulse-steering circuit
  a pulse transition detector (or edge detector) circuit
The pulse transition detector detects a rising (or falling) edge and produces a very short-duration spike.
The pulse transition detector.
S
Q
Q'
CLK
Pulse transition detector
R
Positive-going transition
(rising edge)
CLK
CLK'
CLK*
CLK'
CLK
CLK*
Negative-going transition
(falling edge)
CLK'
CLK
CLK*
CLK
CLK'
CLK*

## Slide 24: D Flip-Flop
D
Q
’
Q
Q
’
D
Q
Symbol for rising-edge
triggered D flip-flop
Symbol for falling-edge
triggered D flip-flop
Clk
rising edges
Clk
falling edges
Internal design: Just invert servant clock rather than master
The triangle means clock input, edge triggered

## Slide 25: D Flip-Flop
Solves problem of not knowing through how many latches a signal travels when C=1
  In figure below, signal travels through exactly one flip-flop, for Clk_A or Clk_B
  Why? Because on rising edge of Clk, all four flip-flops are loaded simultaneously -- then all four no longer pay attention to their input, until the next rising edge. Doesn’t matter how long Clk is 1.
D1
Q1
D2
Q2
D3
Q3
D4
Q4
Y
Clk
Clk_A
Clk_B
Two latches inside each flip-flop

## Slide 26: D-Latch vs. D-Flip-Flop
Latch is level-sensitive: Stores D when C=1
Flip-flop is edge triggered: Stores D when C changes from 0 to 1
  Saying “level-sensitive latch,” or “edge-triggered flip-flop,” is redundant
  Two types of flip-flops -- rising or falling edge triggered.
Comparing behavior of latch and flip-flop:

## Slide 27: Flight-Attendant Call Button Using D Flip-Flop
D flip-flop will store bit
Inputs are Call, Cancel, and present value of D flip-flop, Q
Truth table shown below
Preserve value: if Q=0, make D=0; if Q=1, make D=1
Cancel -- make D=0
Call -- make D=1
Let’s give priority to Call -- make D=1
Circuit derived from truth table, using combinational logic design process
C
all
but
t
on
C
an
c
el
but
t
on
Flight
attendant
call-button
system
Blue
light
D
Q’
Q
Clk
C
all
but
t
on
C
an
c
el
but
t
on
Blue
light
Call
Cancel
Q

## Slide 28: D Flip-Flop
Application: Parallel data transfer.
To transfer logic-circuit outputs X, Y, Z to flip-flops Q1, Q2 and Q3 for storage.
* After occurrence of negative-going transition
Q1 = X*
D
CLK
Q
Q'
Q2 = Y*
D
CLK
Q
Q'
Q3 = Z*
D
CLK
Q
Q'
Combinational logic circuit
Transfer
X
Y
Z

## Slide 29: J-K Flip-Flop
J-K flip-flop: Q and Q' are fed back to the pulse-steering NAND gates.
No invalid state.
Include a toggle state.
  J=HIGH (and K=LOW) a SET state
  K=HIGH (and J=LOW) a RESET state
  both inputs LOW a no change
  both inputs HIGH a toggle
J-K flip-flop.
J
Q
Q'
CLK
Pulse transition detector
K

## Slide 30: J-K Flip-Flop
J-K flip-flop.
Characteristic table.
J
Q
Q'
CLK
Pulse transition detector
K
Q(t+1) = J.Q' + K'.Q

## Slide 31: T Flip-Flop
T flip-flop: single-input version of the J-K flip flop, formed by tying both inputs together.
Characteristic table.
Q(t+1) = T.Q' + T'.Q
T
Q
Q'
CLK
Pulse transition detector
J
C
K
Q
Q'
CLK
T

## Slide 32: Summary
We considered increasingly better bit storage until we arrived at the robust D flip-flop bit storage
D flip-flop
D latch
master
D latch
servant
Dm
Qm
C
m
Ds
D
Clk
Qs’
Cs
Qs
Q
’
Q
S
R
D
Q
C
D latch
Feature: Only loads D value present at rising clock edge, so values can’t propagate to other flip-flops during same clock cycle. Tradeoff: uses more gates internally than D latch, and requires more external gates than SR – but gate count is less of an issue today.
Feature: SR can’t be 11 if D is stable before and while C=1, and will be 11 for only a brief glitch even if D changes while C=1. Problem: C=1 too long propagates new values through too many latches: too short may not enable a store.
Feature: S and R only have effect when C=1. We can design outside circuit so SR=11 never happens when C=1. Problem: avoiding SR=11 can be a burden.
R (reset)
S (set)
Q
SR latch
Feature: S=1 sets Q to 1, R=1 resets Q to 0. Problem: SR=11 yield undefined Q.
S1
R1
S
Q
C
R
Level-sensitive SR latch