## Slide 1: ECE 424 – Introduction to VLSI Design
Emre Yengel
Department of Electrical and Communication Engineering
Fall 2014

## Slide 2: Standard Cell Layout Methodology
Application: Frequency division.
Application: Counter (to be covered in Lecture 13.)
J
C
K
Q
CLK
High
CLK
Q
Divide clock frequency by 2.
J
C
K
QA
CLK
High
J
C
K
QB
High
CLK
QA
QB
Divide clock frequency by 4.

## Slide 3: Multiplexer Based Latches
Negative latch
(transparent when CLK= 0)
Positive latch
(transparent when CLK= 1)
CLK
1
0
D
Q
0
CLK
1
D
Q
For a negative latch, when the clock signal is low, the input 0 of the multiplexer is selected, and the D input is passed to the output.
When the clock signal is high, the input 1 of the multiplexer is selected.

## Slide 4: Multiplexer Based Latches
Transistor-level implementation of a positive latch built by using transmission gates
When CLK is high, the bottom transmission gate is on and the latch is transparent

## Slide 5
To reduce the clock load to two transistors by using implement multiplexers
using NMOS only pass transistor
The advantage of this approach is the reduced clock load of only two NMOS devices. When CLK is high, the latch samples the D input, while a low clock-signal enables the feedback-loop, and puts the latch in the hold mode.
Multiplexer Based Latches

## Slide 6: Master-Slave Edge-Triggered Register
The most common approach for constructing an edge-triggered register is to use a masterslave configuration.
On the low phase of the clock, the master stage is transparent, and the D input is passed to the master stage output QM. During this period, the slave stage is in the hold mode, keeping its previous value using feedback.

## Slide 7: Master-Slave Edge-Triggered Register
A complete transistor-level implementation of a the master-slave positive edge-triggered register

## Slide 8: Dynamic Latches and Registers
A stored value in a static sequential circuit remains valid as long as the supply voltage is applied to the circuit, hence the name static.
The major disadvantage of the static gate is its complexity.
When registers are used in computational structures ,the requirement that the memory should hold state for extended periods of time can be significantly relaxed. This is based on temporary storage of charge on parasitic capacitors.
In this idea, the absence of charge denotes a 0, while its presence stands for a stored 1. A stored value can hence only be kept for a limited amount of time, typically in the range of milliseconds.
If one wants to preserve signal integrity, a periodic refresh of its value is necessary. Hence the name dynamic storage.

## Slide 9: Dynamic Transmission-Gate Edge-triggered Registers
A fully dynamic positive edge-triggered register based on the master-slave concept.
When CLK = 0, the input data is sampled on storage node 1, which has an equivalent capacitance of C1 consisting of the gate capacitance of I1, the junction capacitance of T1, and the overlap gate capacitance of T1.
During this period, the slave stage is in a hold mode, with node 2 in a high-impedance (floating) state.
On the rising edge of clock, the transmission gate T2 turns on, and the value sampled on node 1 right before the rising edge propagates to the output Q
This implementation of an edge-triggered register is very efficient as it requires only 8 transistors.

## Slide 10: Dynamic Transmission-Gate Edge-triggered Registers
Clock overlap is an important concern for this register. During the 0-0 overlap period, the NMOS of T1 and the PMOS of T2 are simultaneously on, creating a direct path for data to flow from the D input of the register to the Q output. This is known as a race condition.
The same is true for the 1-1 overlap region, where an input-output path exists through the PMOS of T1 and the NMOS of T2.

## Slide 11: C2MOS Register - A Clock-Skew Insensitive Approach
The circuit is an ingenious positive edge-triggered register, based on a master-slave concept insensitive to clock overlap.
This circuit is called the C2MOS (Clocked CMOS) register

## Slide 12: C2MOS Register - A Clock-Skew Insensitive Approach
CLK = 0 (CLK = 1): The first tri-state driver is turned on, and the master stage acts as an inverter sampling the inverted version of D on the internal node X. The master stage is in the evaluation mode. The slave section is in a high-impedance mode, or in a hold mode.
The roles are reversed when CLK = 1: The master stage section is in hold mode (M3-M4 off), while the second section evaluates (M7-M8 on). The value stored on CL1 propagates to the output node through the slave stage which acts as an inverter.
positive edge-triggered master-slave register

## Slide 13: C2MOS Register - A Clock-Skew Insensitive Approach
A C2MOS register with CLK-CLK clocking is insensitive to overlap, as long as the rise and fall times of the clock edges are sufficiently small.

## Slide 14: True Single-Phase Clocked Register (TSPCR)
While the C2MOS provides a skew-tolerant solution, it is possible to design registers that only use a single phase clock.
The True Single-Phase Clocked Register (TSPCR), uses a single clock
For the positive latch, when CLK is high, the latch is in the transparent mode. when CLK = 0, both inverters are disabled, and the latch is in hold-mode. Only the pull-up networks are still active, while the pull-down circuits are deactivated.

## Slide 15: Dynamic Latches
A register can be constructed by cascading positive and negative latches.
The main advantage is the use of a single clock phase.
The disadvantage is the slight increase in the number of transistors — 12 transistors are required.
TSPC offers an additional advantage: the possibility of embedding logic functionality into the latches.

## Slide 16: Pipelining: An approach to optimize sequential circuits
Pipelining is used to accelerate the operation of the datapaths in digital processors.
The goal of the presented circuit is to compute log(|a - b|), where both a and b represent streams of numbers.
The minimal clock period Tmin necessary to ensure correct evaluation is given as:
tc-q and tsu are the propagation delay and the set-up time of the register
tpd,logic stands for the worst-case delay path through the combinational network, which consists of the adder, absolute value, and logarithm functions.

## Slide 17: Pipelining: An approach to optimize sequential circuits
Assume that each logic module has an equal propagation delay.
Each logic module is then active for only 1/3 of the clock period, it does no useful computation— during the other 2/3 of the period.
Pipelining is a technique to improve the resource utilization, and increase the functional throughput. Assume that we introduce registers between the logic blocks, as shown below.

## Slide 18: Pipelining: An approach to optimize sequential circuits
This causes the computation for one set of input data to spread over a number of clock periods.
The computation is performed in an assembly-line fashion, hence the name pipeline.
The advantage of pipelined operation becomes apparent when examining the minimum clock period of the modified circuit. The combinational circuit block has been partitioned into three sections, each of which has a smaller propagation delay than the original function. This effectively reduces the value of the minimum allowable clock period:

## Slide 19: Non-Bistable Sequential Circuits
The most important property of a latch circuit is that it has two stable states, and is hence called bistable.
Other regenerative circuits can be catalogued as astable and monostable.
Another interesting regenerative circuit is the Schmitt trigger: its switching threshold is variable and depends upon the direction of the transition (low-to-high or high-to-low). This peculiar feature can come in handy in noisy environments.

## Slide 20: The Schmitt Trigger
A Schmitt trigger is a device with two important properties:
It responds to a slowly changing input waveform with a fast transition time at the output.
The voltage-transfer characteristic of the device displays different switching thresholds for positive- and negative-going input signals. The switching thresholds for the low-to-high and high-to-low transitions are called VM+ and VM-, respectively. The hysteresis voltage is defined as the difference between the two.

## Slide 21: The Schmitt Trigger
One of the main uses of the Schmitt trigger is to turn a noisy or slowly varying input signal into a clean digital output signal.
The “secret” behind the Schmitt trigger concept is the use of positive feedback.

## Slide 22: CMOS Implementation of the Schmitt Trigger
One possible CMOS implementation of the Schmitt trigger is shown below:
The switching threshold of a CMOS inverter is determined by the (kn/kp) ratio between the NMOS and PMOS transistors.
Increasing the ratio results in a reduction of the threshold, while decreasing it results in an increase in VM.

## Slide 23: CMOS Implementation of the Schmitt Trigger
Vin is initially equal to 0, so that Vout = 0 as well.
The feedback loop biases the PMOS transistor M4 in the conductive mode while M3 is off. The input signal connects to an inverter consisting of two PMOS transistors in parallel (M2 and M4) as a pull-up network, and a single NMOS transistor (M1) in the pull-down chain.
This modifies the effective transistor ratio of the inverter to kM1/(kM2+kM4), which moves the switching threshold upwards.
Once the inverter switches, the feedback loop turns off M4, and the NMOS device M3 is activated. This extra pull-down device speeds up the transition and produces a clean output signal with steep slopes.
A similar behavior can be observed for the high-to-low transition. In this case, the pull-down network originally consists of M1 and M3 in parallel, while the pull-up network is formed by M2. This reduces the value of the switching threshold to VM–.